# Anaerobic Treatment of Swine & Dairy Waste

Reduction of Solids Handling
Odor Free Environment
Odor Free Flush Water
Denitrification of Ammonia

Hoffland Environmental, Inc. has developed an efficient, economical covered anaerobic system that not only digests the waste animal solids but also produces sufficient electrical energy to provide a positive payback for the farmer.  The waste animal solids are utilized as a renewable energy resource (certain tax credits are available for this type of equipment).  The waste solids (reference following diagram) flushed from the production floors are concentrated and transferred to a covered mesophilic (temperature 90-100°F) anaerobic digestion basin.  The waste solids in the absence of oxygen and cultured under controlled mesophilic conditions, will biologically decompose forming biogas -principally methane gas.   The methane is collected, pressurized and used as fuel for an engine/generator to produce electricity.  The electricity produced will be adequate to supply all of the electric requirements for the farm plus sell the excess to the power grid.  The amount of electricity produced is proportional to the farms animal population, typically.

5000 Head – Finishers			-	50 KW Continuously

1000 Head – Sow – Farrow to Finish		-	100 KW Continuously

The waste heat produced by the engine is captured and utilized to heat the digester basin to maintain the desired mesophilic microbial growth.  Rapid decomposition of the waste solids occurs in a mesophilic culture.  The size of the anaerobic basin is minimal requiring only 10 days retention, usually sized at 20 days for redundancy.

The effluent from the mesophilic digester is transferred to an aerobic basin to remove the remaining organic components and biologically remove the ammonia.  The ammonia is biologically nitrified and subsequently denitrified to non-toxic benign nitrogen gas (process patented by HEI).

The effluent from the aerobic basin is stored for reuse or distributed through spray fields without the characteristic anaerobic odor.

## Benefits

- Anaerobic odor free operation

- Anaerobic odor free spray fields

- Excess nitrogen nutrients are removed

- No chemicals required

- Sufficient electricity is produced for net payback of equipment

## Typical Operating Cost

Sow Operation	-	(Positive payback from electricity produced, zero electricity bill)

Finisher Operation	-	(Positive payback from electricity produced, zero electricity bill)

## Typical Treatment

Treatment Influent		Treatment Effluent		Reduction

Organic Matter		    20,000 mg/l			       250 mg/l			     99%

Nitrogen			      600 mg/l			        25 mg/l			     97%

Synopsis

Hoffland Environmental, Inc. will supply either the Aerobic or the Anaerobic system.  The following is a brief comparison of the two processes.

|  | Aerobic | Anaerobic |
| --- | --- | --- |
| Capital Cost Operating Cost Tax Credits | Low Capital Cost | Low Operating Cost Available |
| Ammonia | Nitrogen Concentration Reduced | Nitrogen Concentration Reduced |
| Electricity | Consumes | Produces |
| Waste Solids | Solids produced must be stored or distributed daily | Solids flow directly to the digester, no daily labor required |

##### Approximate Cost Excluding Earthwork & Installation

5000 Head Finishing Facility

|  | Aerobic | Anaerobic |
| --- | --- | --- |
| Capital Cost | $100,000 | $200,000 |
| Energy Cost | $5,000/year | Net pay back possible $20,000/year |

15000 Head Finisher or 5000 Sow Facility

|  | Aerobic | Anaerobic |
| --- | --- | --- |
| Capital Cost | $150,000 | $280,000 |
| Energy Cost | $15,000/year | Net pay back possibly $60,000/year |